## Slide 1: UiO NeiC Compute Storage 2022
State of the union

## Slide 2: Compute UiO
System is stable and delivering very well - Openstack on Norwegian Research and Education Cloud (NREC)
  NDGF AHM 2020-1: Delivering pledge
  NDGF AHM 2020-2: Some configuration changes (nfs-exports)
  NDGF AHM 2021-1: Cache, session and compute scratch disk is ssd
Pledge for 2022 is 22.69
  we typically deliver ~28 kHEPSPEC (which roughly corresponds to 2024 pledge)
Support ends 2026 on current hardware
Hardware will be gradually replaced as needed and some more hardware procured to fullfill pledge
Compute and storage will continue in Oslo

## Slide 3: Current status tape
IBM tape system up and running and stable as of Sept-2022
Previous tape system shutdown October-2022
Currently we have 3PB of tape

## Slide 4: Tape in the coming year
We have provisioned money for expansion to meet 6.7PB quota in 2023
We have located a promising source of money for expanding to 10PB in 2024. More money for this is very unlikely to be found.
Expanding past 10PB will require additional slots and therefore budgeting discussions.

## Slide 5: Current status disk
11xHuawei first generation ARM based servers, 176PB each
Only 10 are active due to performance issues with ceph-osd10.grid.uio.no
Performance per node is extremely poor. 170MB/sec average read/write performance.
Due to read/write patterns, we generally never achieve greater than 1GB/s aggregate performance.
Support agreement on these servers runs out in mid-2023, we will not renew.

## Slide 6: Disk in the coming year
Options
  Copy Sweden
  Build something similar to Sweden and make the nodes denser
  Deploy a storage system and VMs similar to UiB

## Slide 7: Copy Sweden
Low cost per PB
Hit-by-a-bus issues (only one person at UiO who will manage)
No meaningful vendor support
It doesn’t scale well for us, we can do much with Ansible, but growing the system means more nodes to manage.
Will not scale performance by adding more nodes unless read/write patterns support enough entropy
This is our fall-back option

## Slide 8: Higher density nodes
Similar to Sweden, but bigger nodes
Lower cost per petabyte
Less management
“violates” desired node size
Long rebuild/replacement times
Less than optimal, but very inexpensive
Much easier to fit in the racks

## Slide 9: Storage Systems and VMs
MUCH MUCH cheaper per node (this has to do with internal UiO creative budgeting more than cost per PB)
Offsets issues with management as we have an internal storage department who can manage the storage side of the systems
Can deploy and redeploy VMs entirely with Terraform and Ansible… possibly Kubernetes
Much higher aggregate bandwidth scalability as read write patterns are managed. It doesn’t depend as much on entropy
Rebuild times are far less. A lost dcache node is recovered in minutes rather than days.
Reboots in seconds rather than minutes.

## Slide 10: Current prospects – Dell PowerVault
all the problems with individual servers, none of the benefits of unified storage systems.
Major scalability both in performance and management
Maximum bandwidth per controller 10Gb/s, not a cluster
Behaves like a DAS which would only add management headaches

## Slide 11: Current Prospects – IBM Spectrum
Highest performance per spindle tested so far.
110 spindles per cabinet.
We have a whole department for just IBM Spectrum.
We expect extremely low prices, possibly less than the cost for raw drives due to agreements.
Scaling drawers only increases capacity, not necessarily performance.
Additional controllers are needed to scale performance.
Based on Power architecture which is a second-class (possibly third) citizen on Linux.
Everything from IBM is pay-walled which means scripts to automatically deploy updates will need user intervention.
IBM doesn’t really care about one customer with odd needs. If we need features, we’ll have to beg and wait.
Conslusion : Great solution if the price fits… don’t like the lack of leverage

## Slide 12: Current prospects continued – Huawei PacificStor
Easiest to manage.
3% lower performance per spindle than IBM.
Incredible physical chassis design.
Fastest and cheapest support.
Scales in performance as well as capacity while adding drawers as additional nodes add additional controllers.
They added features and patches just to do the PoC, Huawei sees any shortcomings in their system as embarrassing and acts rapidly to fix them.
Works best when connected with RDMA (Infiniband or RoCEv2)
NFS implementation is fairly “vanilla linux” and has terrible issues with massive directories.
Huawei native cluster client requires RDMA
4+2 and 8+2 Erasure coding has almost identical performance. I’ve asked for numbers for 12+2.
Huawei has the lowest erasure coding latency I’ve evaluated thus far
Conclusion: Technically the best solution so far, price is probably good, support is “they are willing to do anything”

## Slide 13: Current prospects - Hitatchi
Next and last to evaluate
Expectations
  Possibly higher performance drives (they make their own)
  Heavier use of SSD for metadata which should show great performance benefits.
  High performance.
  Good horizontal scaling, equal to or better than IBM. Maybe equal to or better than Huawei.
Hitachi is very competitive for pricing but already is suggesting it may cost more.
No conclusions yet

## Slide 14: Storage conclusion
We have the money in hand
We are waiting on Hitatchi results to garner the tender
We are prepared to streamline the tender and bidding.
We want to have disks on premises no later than 15-Jan

## Slide 15: Coming year
Big network downtime at UiO
  Switching out 25Gb/s TOR switches for 100Gb/s
  Implementation of RoCEv2 (reliable ethernet… IE moving from Ethernet to converged ethernet with at least support for DCBx, LLQ and PFC)
  We will finally have redundant top of rack switches.
  Trying to push for moving the uplink to a clustered switch as we don’t have a backup link and we want to be able to maintain the switches. We haven’t updated firmware on the existing switching in a long time.
  Week or two outage while transitioning

## Slide 16: Storage will stay at UiO, not Sigma2
This was a major point of contention.
Sigma2 is a national mandate to move all this stuff into a centralized place up north.
They didn’t want to take the tape.
They wanted to charge us more money for disk than we were willing to pay.
We have now more or less guaranteed UiO as the long term home for Atlas storage.
Discussions have arisen about possibly centralizing storage in a NeiC partner country but that discussion isn’t for a few years.

## Slide 17: Automation of everything
The goal for UiO Disk and Tape in 2023 is automatic everything
Downtimes will be requested by script
Machines will update firmware, OS and all else via script.
We want to move all dCache everything to Ansible/Terraform/Kubevirt deployment/maintenance. No more changing things on the CLI.
Everything in Git